## Slide 1
RESEARCH PLAN
Selfish routing, autonomous intersections, and non-monetary control
Timestamp incentives turn intersections into a non-monetary routing lever.
A research-program deck based on Saltan's thesis summary and the proposed direction: robust, fair, mixed-autonomy timestamp incentives for selfish routing.
68.2%
THESIS GAP CLOSURE
Sioux Falls, high-intervention bounds
71%
LATER ARXIV V2
reported upper efficiency-gap reduction
5
RESEARCH WORKSTREAMS
dynamic, mixed, fair, private, scalable
90
EXECUTION DAYS
from reproduction to first draft
Source: ResearchPlan.md, sections 1, 8, 10, 12
01

## Slide 2
CORE MOVE
The thesis replaces tolls with controlled waiting time.
Drivers still choose selfishly. The planner changes the waiting-time signal they experience at intersections, making socially helpful routes feel cheaper and overused routes feel more expensive.
MONETARY TOLL
Pay more to use this route.
Hard to administer, politically fragile, and often equity-sensitive.
TIMESTAMP INCENTIVE
Wait less on helpful routes.
Uses a capability autonomous intersections already need: ordering vehicle requests safely.
same incentive logic,
different currency
Source: ResearchPlan.md, sections 1-2
02

## Slide 3
MECHANISM LOOP
The mechanism changes perceived path costs, not driver objectives.
1
Drivers choose routes
selfish travel-time minimization
>
2
User equilibrium emerges
Wardrop behavior can be inefficient
>
3
Intersections observe requests
timestamps, movement, queue state
>
4
Planner offsets timestamps
advance or delay effective request time
>
5
Path costs shift
node costs become route-dependent
>
6
Flow redistributes
total system travel time decreases
The intervention is local in implementation but network-level in effect: it modifies route costs at conflict points where queues already create delay.
Source: ResearchPlan.md, section 2
03

## Slide 4
TWO MECHANISMS
SPBS proves the idea; timestamp offsets make it network-scale.
MECHANISM A
Strategic Priority-Based Scheduling
Introduced on Pigou-type networks
Assigns route-dependent priority scores
Higher priority for socially preferred routes
SUMO simulation supports qualitative effect
upper node delay = w - p
lower node delay = w + p
MECHANISM B
Timestamp-Offset Incentives
Generalizes to path-dependent node costs
Advances or delays effective request timestamps
Keeps local safety scheduling intact
Supports network-level bilevel optimization
c_v^p(f_v, u_v^p) = c_v(f_v) + u_v^p
Source: ResearchPlan.md, section 3
04

## Slide 5
WHY IT REMAINS ANALYZABLE
Additive node costs preserve a tractable equilibrium model.
Path cost = link travel time + node delay + timestamp offset
offsets enter as structured, path-dependent node costs
Lower level
Wardrop equilibrium under modified path costs
Potential structure
equilibrium exists; social cost is essentially unique
Upper level
planner chooses bounded offsets to reduce social cost
Bilevel design
01
Choose incentives u
anticipate response
02
Compute equilibrium f(u)
evaluate cost
03
Minimize social cost
Source: ResearchPlan.md, sections 3 and 5
05

## Slide 6
BENCHMARK EVIDENCE
Sioux Falls evidence shows the idea has real network leverage.
User equilibrium
8.04M min
baseline
Timestamp incentives
7.84M min
high-intervention
System optimum
7.75M min
benchmark
68.2%
thesis-reported gap closure
71%
later arXiv v2 reported upper reduction
The slide does not claim deployment readiness. It claims enough leverage to justify testing robustness, fairness, partial adoption, privacy, and scalable solvers.
Source: ResearchPlan.md, sections 4 and 8
06

## Slide 7
OPEN GAPS
The next paper relaxes the clean assumptions without losing control.
Static routing
make incentives online and stable
Full route observability
work with prefixes or privacy-noised beliefs
Separable node costs
account for spillback and lane coupling
High V2I capability
estimate penetration thresholds
Fairness under-modeled
bound repeated delay burdens
Costly bilevel search
differentiate, decompose, or learn surrogates
Source: ResearchPlan.md, section 6
07

## Slide 8
RESEARCH PROGRAM
Five workstreams turn the thesis into a publishable agenda.
Robust, fair,
mixed-autonomy incentives
RQ1
Dynamic online control
rolling horizons, incidents, prediction error
RQ2
Mixed autonomy
CAV penetration, compliance, indirect response
RQ3
Fairness-aware delay
OD budgets, max-min welfare, equity curves
RQ4
Privacy and misreporting
prefix beliefs, audits, spoofing resistance
RQ5
Scalable bilevel algorithms
implicit gradients, surrogates, decomposition
Source: ResearchPlan.md, section 8
08

## Slide 9
FIRST PAPER
Stay focused: mixed autonomy plus fairness is the first publishable step.
INCLUDE
heterogeneous controllability
connected compliant, strategic,
and non-connected users
INCLUDE
fairness-constrained timestamp bounds
OD delay budgets, worst-case burdens,
efficiency-equity curves
DEFER
dynamic spillback
save receding-horizon and capacity
coupling for paper 2 or 4
DEFER
privacy and strategic reporting
route-prefix and misreporting protocols
can become paper 3
Core claim
Bounded timestamp incentives can reduce routing inefficiency with partial connected-vehicle penetration, if fairness constraints are built into the planner.
Pigou
Braess
Sioux Falls
Source: ResearchPlan.md, section 9
09

## Slide 10
METHOD STACK
Pair equilibrium theory with simulation-backed calibration.
Model
mixed connected/non-connected users; path-dependent node costs
Equilibrium
Wardrop assignment with bounded timestamp offsets
Optimization
warm-started Frank-Wolfe plus constrained upper-level search
Experiments
Pigou, Braess, Sioux Falls, and one grid network
Metrics
travel time, delay burden, CAV threshold, fairness-constrained PoA
Baselines
FCFS
SPBS
unconstrained timestamp
fairness-constrained timestamp
marginal-cost tolling
Source: ResearchPlan.md, sections 5 and 9
10

## Slide 11
90-DAY PLAN
Move from reproduction to a conference-paper draft in four phases.
Days 1-15
Reproduce and simplify
Pigou/Braess equations, Wardrop solver, technical memo
>
Days 16-30
Build Sioux Falls baseline
BPR links, node costs, UE/SO efficiency gap
>
Days 31-60
Add timestamp incentives
bounded offsets, constrained optimizer, one deep extension
>
Days 61-90
Experiments and draft
sensitivity plots, propositions, 6-8 page conference version
Recommended first extension: fairness constraints under mixed autonomy.
Source: ResearchPlan.md, section 10
11

## Slide 12
THESIS-LEVEL ROADMAP
The roadmap compounds from fairness to dynamic, private, and scalable control.
Paper 1
Fair mixed-autonomy timestamp incentives
Paper 2
Dynamic online timestamp control
Paper 3
Privacy and strategic reporting
Paper 4
Spillback-aware theory
Paper 5
Scalable bilevel algorithms
Final takeaway
The opportunity is not only to improve the Sioux Falls result. It is to make intersection scheduling credible as a real incentive mechanism for heterogeneous urban networks.
Intersection scheduling can be used as an incentive mechanism.
Source: ResearchPlan.md, sections 11-12
12